Physics 534

Adding Vectors by Components: An Introduction

- Split the following vectors into their horizontal and vertical components:

  - 25 m/s, [S15°E]

  - 8.0 N, [W 30° S]

  - A plane is flying at a velocity of 750 km/h in the [N 40° W].

- Two men are pulling a heavy cart, as is illustrated below (this is a view from above).  What is the net (resultant) force being applied to the cart?

- A plane is flying due East at a velocity of 175 m/s.  The wind blows at a velocity of

65 m/s [N65°E]. What is the resultant velocity of the plane?

- During a rally in the desert, a team leaves the base camp and travels 58 km [E], 65 km

[S55°E] and then 120 km [W35°N].  At that point, their car breaks down.  A helicopter then leaves base camp to come to their rescue.

  - Give the vector that represents the displacement of the helicopter, as it goes to rescue the participants.

  - Give the vector that represents the displacement of the helicopter as it returns to base camp.

Answers to: Adding Vectors by Components: An Introduction

| 1) | a) | x: 6.47 m/s y: - 24.1 m/s |  |
| --- | --- | --- | --- |
|  | b) | x: - 6.9 m/s y: - 4.0 m/s |  |
|  | c) | x: - 482 km/h |  |
|  |  | y: 575 km/h |  |
|  | d) | x: 68.0 m y: 31.7 m |  |
|  | e) | x: - 7.25 N y: 3.38 N |  |
| 2) |  | For the vector on the “left” x: - 162 N y: 446 N (- 162 N, 446 N) | For the vector on the “right” x: 402 N y: 337 N (402 N, 337 N) |
|  |  | Add the vectors: (- 162 N, 446 N) + ( 402 N, 337 N) R:( 240 N, 783 N) Ans: 819 N, 73° | Sketch: |

| 3) |  | Plane: (175 m/s, 0) Wind: (58.9 m/s, 27.5 m/s) Add the vectors: (175 m/s, 0) + (58.9 m/s, 27.5 m/s) R (233.9 m/s, 27.5m/s) Ans: 236 m/s [E 7° N] | Sketch: |
| --- | --- | --- | --- |
| 4) | a) | 1st displacement: (58 km, 0) 2nd displacement: (53.2 km, - 37.3 km) 3rd displacement: (- 98.3 km, 68.8 km) For part a), we are looking for the resultant. Add the vectors: (58 km, 0 km) + (53.2 km, - 37.3 km) + (- 98.3 km, 68.8 km) R: (12.9 km, 31.5 km) Ans: 34 km [E 68° N] | Sketch of the resultant: |
|  | b) | For part b), we are looking for the return displacement vector (not the resultant). θ = 180° - 68° - 90° = 22° Ans: 34 km [S 22° W] | Sketch of the resultant: |

# Text boxes

25°

75 m

8.0 N

65°

40.0°

70.0°

525 N

475 N

240 N

783 N

θ

233.9 m/s

27.5 m/s

θ

12.9 km

31.5 km

θ

θ

31.5 km

12.9 km